## Slide 2
PCIE发展

## Slide 3
1981
1987
1989
1990
1998
1997
2002
2010
2006
2014
2019
2021
1988
ISA (Industry Standard Architecture)
MCA (Micro Channel Architecture)
VLB (VESA Local Bus)
PCI (Peripheral Component Interconnect)
PCI-X (Peripheral Component Interconnect eXtended)
AGP (Accelerated Graphics Port)
PCI Express (Peripheral Component Interconnect Express)
PCI Express(3.0)
PCI Express(2.0)
PCI Express(4.0)
PCI Express(5.0)
PCI Express(6.0)
EISA (Extended Industry Standard Architecture)

## Slide 4
版本 | 时间 | 编码 | 原始速度 | 带宽 |  |  |  | 
 |  |  |  | ×1 | ×2 | ×4 | ×8 | ×16
1 | 2003 | 8b/10b | 2.5 GT/s | 250 MB/s | 0.50 GB/s | 1.0 GB/s | 2.0 GB/s | 4.0 GB/s
2 | 2007 | 8b/10b | 5.0 GT/s | 500 MB/s | 1.0 GB/s | 2.0 GB/s | 4.0 GB/s | 8.0 GB/s
3 | 2010 | 128b/130b | 8.0 GT/s | 984.6 MB/s | 1.97 GB/s | 3.94 GB/s | 7.88 GB/s | 15.8 GB/s
4 | 2017 | 128b/130b | 16.0 GT/s | 1969 MB/s | 3.94 GB/s | 7.88 GB/s | 15.75 GB/s | 31.5 GB/s
5 | 2019 | NRZ 128b/130b | 32.0 GT/s | 3938 MB/s | 7.88 GB/s | 15.75 GB/s | 31.51 GB/s | 63.0 GB/s
6 | 2021 | PAM4 & FEC 128b/130b | 64.0 GT/s | 7877 MB/s | 15.75 GB/s | 31.51 GB/s | 63.02 GB/s | 126.03 GB/s